Components:
5V Voltage regulator

This voltage regulator is for the Raspberry Pi.

FIXME I'm going to get this 5V regulator. I'll have to say how it goes. Also say if you got any pins to solder to this board or not

this looks good:
http://www.hobbytronics.co.uk/electronic-components/voltage-regulators/voltage-regulator-5v/d24v22f5-5v-step-down-regulator

### 5V 2.5A Step-Down Voltage Regulator D24V22F5
This small synchronous switching step-down (or buck) regulator takes an input voltage of up to 36 V and efficiently reduces it to 5 V. The board measures only 0.7″ × 0.7″ yet delivers a typical continuous output current of up to 2.5 A and features reverse voltage protection. Typical efficiencies of 85% to 95% make this regulator well suited for powering moderate loads like sensors or small motors. An optional shutdown pin enables a low-power state with a current draw of around 20 μA to 350 μA, depending on the input voltage, and a power-good output indicates when the regulator cannot adequately maintain the output voltage.
These regulators have a typical quiescent (no load) current draw of around 1 mA, and an enable pin can be used to put the boards in a low-power state that reduces the quiescent current to approximately 5 µA to 10 µA per volt on VIN.
The modules have built-in reverse-voltage protection, short-circuit protection, a thermal shutdown feature that helps prevent damage from overheating, and a soft-start feature that reduces inrush current.
Features
- Input voltage: 6 V to 38 V (see below for more details on the regulator’s dropout voltage, which affects the low end of the operating range)
- Fixed 5 V output (with 4% accuracy)
- Typical maximum continuous output current: > 2.5 A
- Integrated reverse-voltage protection, over-current protection, over-temperature shutoff, soft-start, and under-voltage lockout
- Typical efficiency of 85% to 95%, depending on input voltage and load; the switching frequency automatically changes at light loads to maintain high efficiencies
- 1 mA typical no-load quiescent current; this can be reduced to approximately 5 µA to 10 µA per volt on VIN by disabling the board
- “Power good” output indicates when the regulator cannot adequately maintain the output voltage
- Compact size: 0.7″ × 0.7″ × 0.31″ (17.8 mm × 17.8 mm × 8 mm)
- Two 0.086″ mounting holes for #2 or M2 screws
These buck regulators have five main connection points for five different electrical nodes: power good (PG), enable (EN), input voltage (VIN), ground (GND), and output voltage (VOUT). The board also features a second ground connection point off the main row of connections that might be convenient for applications where you are soldering wires directly to the board rather than using it in a breadboard.
The input voltage, VIN, powers the regulator and can be supplied with voltages up to 38 V. The effective lower limit of VIN is VOUT plus the regulator’s dropout voltage, which varies approximately linearly with the load (see below for a graph of dropout voltages as a function of the load).
The regulator is enabled by default: a 270 kΩ pull-up resistor on the board connects the EN pin to reverse-protected VIN. The EN pin can be driven low (under 1 V) to put the board into a low-power state. The quiescent current draw in this sleep mode is dominated by the current in the pull-up resistor from EN to VIN and by the reverse-voltage protection circuit, which altogether will draw between 5 µA and 10 µA per volt on VIN when EN is held low. If you do not need this feature, you should leave the EN pin disconnected.
The “power good” indicator, PG, is an open-drain output that goes low when the regulator’s output voltage falls below around 85% of the nominal voltage and becomes high-impedance when the output voltage rises above around 90%. An external pull-up resistor is required to use this pin.

Other ideas:
http://www.dx.com/p/hobbywing-5v-6v-3a-switch-mode-ultimate-bec-ubec-15149#.VuCzLeinxJ8
http://www.dx.com/p/8s-5a-switch-mode-ultimate-bec-ubec-45214#.VuFjIjp6elN
This should be OK as 5V voltage regulator: http://uk.rs-online.com/web/p/products/0633026/