Components:
Batteries and charger
# Batteries
These are 4400 mAh batteries for a total voltage of 11.1V (3.7 x 3)
http://www.ebay.com/itm/SAMSUNG-Rechargeable-Li-ion-Battery-18650-22F-11-1V-4400MAH-3S2P-6pcs-cell-/220999843383?hash=item33749dfe37
# Battery charger
It charges batteries and balances battery charge so that there is no risk that a battery ends up overcharged with the other batteries undercharged. It protects the batteries from overcharge, overcurrent and short circuit.
http://www.ebay.com/itm/Balance-BMS-Protected-Module-PCM-3S-4A-11-1V-Li-ion-Li-Po-Battery-3S4W007-/221791091395?hash=item33a3c77ac3

No	Test Item		Criterion
1	Voltage	Charging voltage	DC:13.5-15V CC/CV
		Balance voltage for single cell	4.2V
2	Current	Balance current for single cell	42mA
		Current consumption	≤15μA
		Maximal continuous charging current	N/A
		Maximal continuous Discharging current	4.5A
3	Over charge Protection	Over charge detection voltage	4.350±0.025V
		Over charge detection delay time	1S
		Over charge release voltage	4.15±0.05V
4	Over discharge protection	Over discharge detection voltage	2.7±0.08V
		Over discharge detection delay time	100mS
		Over discharge release voltage	3.0±0.1V
5	Over current protection	Over current detection voltage	200±25mV
		Over current detection current	17±3A
		Detection delay time	10ms
		Release condition	Cut load
6	Short Circuit protection	Detection condition	Exterior short circuit
		Detection delay time	≤600us
		Release condition	Cut load
7	Resistance	Protection circuitry（MOSFET）	≤15mΩ
8	Temperature	Operating Temperature Range	-40～+85℃
		Storage Temperature Range	-40～+125℃

# Test results
FIXME I'll have to say how it goes